## Slide 1: CUDA Video UnScrambler
Recovering scrambled video using GPU brute-force search
Jetson Nano – CUDA + OpenCV

## Slide 2: Context
Old Pay-TV scrambling by line permutation
Goal: recover key (r,s) and unscramble video

## Slide 3: Scrambling Principle
scrambledIndex = (r + (2s+1)*idLine) % size
Block sizes are powers of two

## Slide 4: Architecture
1) Read scrambled frame
2) CPU: generate 32768 permutations
3) GPU: score keys
4) GPU: unscramble frames
5) Display + save output

## Slide 5: Permutation Generation
Iterative power-of-two blocks
Implements guideline formula exactly

## Slide 6: Brute-Force Key Search
256 values of r × 128 values of s = 32768 keys
Fully exhaustive search

## Slide 7: Similarity Scoring
Euclidean distance between adjacent lines
Lower score = correct key

## Slide 8: CUDA Kernel: scoreKeysKernel
One block = one key
128 threads compute SSD in parallel
Shared memory reduction

## Slide 9: CUDA Kernel: unscrambleKernel
Thread-per-pixel remapping
Coalesced memory access for speed

## Slide 10: Optimizations
Pixel sampling (stride 4)
Batching keys
Shared memory reductions
Grayscale scoring

## Slide 11: Code Structure
unscrambler.cu: kernels, main loop
CMakeLists.txt: CUDA + OpenCV

## Slide 12: Results
Correct key recovered
Real-time playback
Clean output video

## Slide 13: Conclusion
GPU-accelerated unscrambler
Efficient, accurate, real-time